## Slide 1
Ronald van Buuren
May 2023
SCHOOL OF ENGINEERING, ELECTRICAL AND ELECTRONIC ENGINEERING
NETWORKS 4_ Week D_

## Slide 2: net4 program by week
1st order RC networks – discharging – DC source
1st order RC networks – charging –DC source
RL networks – Steady-state DC
RL networks – Switched DC source
RC & RL networks – complementary solution
<spare week>
Sample Exam

## Slide 3: Capacitor & inductor relations
 | Capacitor | Inductor
Voltage |  | 
Current |  | 
Power |  | 
Energy |  | 
Energy stored in: | Electric field | Magnetic field
 | Capacitor | Inductor
Voltage |  | 
Current |  | 
Power |  | 
Energy |  | 
Energy stored in: | Electric field | Magnetic field

## Slide 4: week c: DC Steady State
At we close the switch
Hoe groot zijn ix en vx op ?

## Slide 5: week c: dc steady state
Equivalent circuit at
ix = V / (R1 + R2) = 1 A
vx = R2 / (R1 + R2) x V = 5 V (voltage division)

## Slide 6: RL circuits
Find expressions for i(t) and v(t) for t > 0
probably a differential equation?

## Slide 7: RL circuits - using KVL
KVL: Write individual voltages with polarities
  +VS
  vR = -i(t)·R
  vL = -Ldi/dt
Write KVL:
VS - i(t)·R - Ldi/dt = 0
Re-arrange:
i(t) + =
Haven’t we seen this before?

## Slide 8: RL circuits - using KVL
i(t) + =
Remember week B, charging a capacitor (and KCL):
Educated guess i=K1+K2est

## Slide 9: RL circuits - using KVL
i(t) + =
insert i(t) = K1+K2est:
K1+K2est + sK2est =

## Slide 10: RL circuits - using KVL
K1+K2est + sK2est =

## Slide 11: RL circuits - using KVL
K1+K2est + sK2est =
K1 = = 2 A
s = - = -500 s-1
K2?
Aha, initial condition around t=0
i(t=0-) = 0
i(t=0+) = 0 (i must be continuous)
So, K2 = -K1 = -2 A
i(t) = K1+K2est
i(t) = 2-2e-500t A

## Slide 12
i(t) = 2-2e-500t A

## Slide 13: RL circuits - using KVL
Final step: find v(t)
so (how’s your Math?)
0.1*d(2-2e-500t)/dt
v(t) = 100e-500t V
i(t) = 2-2e-500t A

## Slide 15: Recipe for simple circuits (RC & RL)
Use one of Kirchhoff’s laws to get a circuit equation
If the equation has integrals, differentiate all terms to get a pure differential equation
Try a solution of the type
  Enter it into the equation
  Solve for &
  Use starting conditions (t=0-, t=0+) to get
Write the now fully known equation
  i.e. using R, L, C, t

## Slide 16: RL circuits – now via KcL
Find expressions for i(t) and v(t) for t > 0
surely another differential equation

## Slide 17: RL circuits – now via KcL
Write individual currents with polarities
  iR = (VS – v(t)) / R
  iL = -
Apply KCL: sum = 0 @ node
[VS - v(t)]/R - = 0
Differentiate to remove integral:
0 - - v(t) = 0
Rearrange:
+ = 0

## Slide 18: RL circuits – now via KcL
+ = 0
K1+K2est + sK2est = 0
K1 = 0
s = -
Initial: v(0+) = VS = 100 V
K2 = 100 V
Try v=K1+K2est
v(t) = 100e-500t V

## Slide 19: RL circuits – now via KcL
v(t) = 100e-500t V
Final step: find i(t)
i(t) is the same everywhere, so choose R to get it using Ohm’s law
i(t) = (Vs – v(t)) / R
= (100 - 100e-500t) / 50
i(t) = 2 - 2e-500t A

## Slide 20: RL circuits – via DC steady state
will follow later

## Slide 21: Exercise
Find i(t) and v(t) for t>0

## Slide 22: problems for the exercises session
P4.31
P4.33
P4.34
P4.37
P4.39
P4.42